Virtual Memory Systems and Dynamic Memory Allocation
Computer Systems
Nov. 5, 2018
Troels Henriksen
Based on slides by:
Randal E. Bryant and David R. O’Hallaron

---
Today
Simple memory system example
Case study: Linux memory system
Memory mapping
Dynamic Allocation
Bonus: Implicit Free Lists

---
Review of Symbols
Basic Parameters
N = 2n : Number of addresses in virtual address space
M = 2m : Number of addresses in physical address space
P = 2p : Page size (bytes)
Components of the virtual address (VA)
TLBI: TLB index
TLBT: TLB tag
VPO: Virtual page offset
VPN: Virtual page number
Components of the physical address (PA)
PPO: Physical page offset (same as VPO)
PPN: Physical page number
CO: Byte offset within cache line
CI: Cache index
CT: Cache tag

---
Simple Memory System Example
Addressing
14-bit virtual addresses
12-bit physical address
Page size = 64 bytes
13
12
11
10
9
8
7
6
5
4
3
2
1
0
VPN
VPO
Virtual Page Offset
Virtual Page Number
11
10
9
8
7
6
5
4
3
2
1
0
PPN
PPO
Physical Page Number
Physical Page Offset

---
1. Simple Memory System TLB
16 entries
4-way associative
TLBT
TLBI
13
12
11
10
9
8
7
6
5
4
3
2
1
0
VPO
VPN
Set
Tag
PPN
Valid
Tag
PPN
Valid
Tag
PPN
Valid
Tag
PPN
Valid
0
03
–
0
09
0D
1
00
–
0
07
02
1
1
03
2D
1
02
–
0
04
–
0
0A
–
0
2
02
–
0
08
–
0
06
–
0
03
–
0
3
07
–
0
03
0D
1
0A
34
1
02
–
0

---
2. Simple Memory System Page Table
Only show first 16 entries (out of 256)
VPN
PPN
Valid
VPN
PPN
Valid
00
28
1
08
13
1
01
–
0
09
17
1
02
33
1
0A
09
1
03
02
1
0B
–
0
04
–
0
0C
–
0
05
16
1
0D
2D
1
06
–
0
0E
11
1
07
–
0
0F
0D
1

---
3. Simple Memory System Cache
16 lines, 4-byte block size
Physically addressed
Direct mapped
CT
CI
CO
11
10
9
8
7
6
5
4
3
2
1
0
PPN
PPO
Idx
Tag
Valid
B0
B1
B2
B3
Idx
Tag
Valid
B0
B1
B2
B3
0
19
1
99
11
23
11
8
24
1
3A
00
51
89
1
15
0
–
–
–
–
9
2D
0
–
–
–
–
2
1B
1
00
02
04
08
A
2D
1
93
15
DA
3B
3
36
0
–
–
–
–
B
0B
0
–
–
–
–
4
32
1
43
6D
8F
09
C
12
0
–
–
–
–
5
0D
1
36
72
F0
1D
D
16
1
04
96
34
15
6
31
0
–
–
–
–
E
13
1
83
77
1B
D3
7
16
1
11
C2
DF
03
F
14
0
–
–
–
–

---
Address Translation Example #1
Virtual Address: 0x03D4
VPN ___	TLBI ___	TLBT ____	TLB Hit? __	Page Fault? __ PPN: ____
Physical Address
CO ___	CI___	CT ____	Hit? __ Byte: ____
TLBT
TLBI
13
12
11
10
9
8
7
6
5
4
3
2
1
0
0
1
0
1
0
0
0
0
0
1
1
1
1
0
VPN
VPO
N
0x0F
0x3
0x03
0x0D
Y
CI
CT
CO
11
10
9
8
7
6
5
4
3
2
1
0
0
0
1
1
0
1
0
1
0
1
0
0
PPN
PPO
0
0x5
0x0D
Y
0x36

---
Address Translation Example #2
Virtual Address: 0x0020
VPN ___	TLBI ___	TLBT ____	TLB Hit? __	Page Fault? __ PPN: ____
Physical Address
      CO___	CI___	CT ____	Hit? __ Byte: ____
TLBT
TLBI
13
12
11
10
9
8
7
6
5
4
3
2
1
0
1
0
0
0
0
0
0
0
0
0
0
0
0
0
VPN
VPO
0
0x00
0x00
0x28
N
N
CI
CT
CO
11
10
9
8
7
6
5
4
3
2
1
0
1
0
1
0
0
0
1
0
0
0
0
0
PPN
PPO
0
0x28
N
Mem
0x8

---
Today
Simple memory system example
Case study: Linux memory system
Memory mapping
Dynamic allocation
Bonus: Implicit free lists

---
Virtual Address Space of a Linux Process
Process-specific data
 structs (ptables,
task and mm structs, kernel stack)
Different for each process
Kernel
virtual
memory
Physical memory
Identical for each process
Kernel code and data
User stack
%rsp
Memory mapped region
for shared libraries
Process
virtual
memory
brk
Runtime heap (malloc)
Uninitialized data (.bss)
Initialized data (.data)
Program text (.text)
0x00400000
0

---
Linux Organizes VM as Collection of “Areas”
Process virtual memory
vm_area_struct
task_struct
mm_struct
vm_end
vm_start
mm
pgd
vm_prot
vm_flags
mmap
Shared libraries
vm_next
vm_end
pgd:
Page global directory address
Points to L1 page table
vm_prot:
Read/write permissions for
this area
vm_flags
Pages shared with other processes or private to this process
vm_start
Data
vm_prot
vm_flags
Text
vm_next
vm_end
vm_start
vm_prot
vm_flags
0
vm_next

---
Linux Page Fault Handling
Process virtual memory
vm_area_struct
vm_end
vm_start
vm_prot
vm_flags
shared libraries
vm_next
1
Segmentation fault:
accessing a non-existing page
read
vm_end
vm_start
3
data
vm_prot
read
Normal page fault
vm_flags
text
vm_next
Protection exception:
e.g., violating permission by writing to a read-only page (Linux reports as Segmentation fault)
2
write
vm_end
vm_start
vm_prot
vm_flags
vm_next

---
Today
Simple memory system example
Case study: Linux memory system
Memory mapping
Dynamic allocation
Bonus: Implicit free lists

---
Memory Mapping
VM areas initialized by associating them with disk objects.
Process is known as memory mapping.
Area can be backed by (i.e., get its initial values from) :
Regular file on disk (e.g., an executable object file)
Initial page bytes come from a section of a file
Anonymous file (e.g., nothing)
First fault will allocate a physical page full of 0's (demand-zero page)
Once the page is written to (dirtied), it is like any other page
Dirty pages are copied back and forth between memory and a special swap file.

---
Sharing Revisited: Shared Objects
Physical
memory
Process 2
virtual memory
Process 1
virtual memory
Process 1 maps the shared object.
Shared
object

---
Sharing Revisited: Shared Objects
Physical
memory
Process 2
virtual memory
Process 1
virtual memory
Process 2 maps the shared object.
Notice how the virtual addresses can be different.
Shared
object

---
Sharing Revisited:
Private Copy-on-write (COW) Objects
Physical
memory
Process 2
virtual memory
Process 1
virtual memory
Two processes mapping a private copy-on-write (COW) object.
Area flagged as private copy-on-write
PTEs in private areas are flagged as read-only
 Private
copy-on-write
area
Private
copy-on-write object

---
Sharing Revisited:
Private Copy-on-write (COW) Objects
Instruction writing to private page triggers protection fault.
Handler creates new R/W page.
Instruction restarts upon handler return.
Copying deferred as long as possible!
Physical
memory
Process 2
virtual memory
Process 1
virtual memory
Copy-on-write
Write to private
copy-on-write
page
Private
copy-on-write object

---
The fork Function Revisited
VM and memory mapping explain how fork provides private address space for each process.
To create virtual address for new new process
Create exact copies of current mm_struct, vm_area_struct, and page tables.
Flag each page in both processes as read-only
Flag each vm_area_struct in both processes as private COW
On return, each process has exact copy of virtual memory
Subsequent writes create new pages using COW mechanism.

---
The execve Function Revisited
To load and run a new program a.out in the current process using execve:
Free vm_area_struct’s and page tables for old areas
Create vm_area_struct’s and page tables for new areas
Programs and initialized data backed by object files.
.bss and stack backed by anonymous files .
Set PC to entry point in .text
Linux will fault in code and data pages as needed.
Private, demand-zero
User stack
libc.so
Memory mapped region
for shared libraries
.data
Shared, file-backed
.text
Runtime heap (via malloc)
Private, demand-zero
Private, demand-zero
Uninitialized data (.bss)
a.out
Initialized data (.data)
.data
Private, file-backed
Program text (.text)
.text
0

---
User-Level Memory Mapping
void *mmap(void *start, int len,
        int prot, int flags, int fd, int offset)
Map len bytes starting at offset offset of the file specified by file description fd, preferably at address start
start: may be 0 for “pick an address”
prot: PROT_READ, PROT_WRITE, ...
flags: MAP_ANON, MAP_PRIVATE, MAP_SHARED, ...
Return a pointer to start of mapped area (may not be start)

---
User-Level Memory Mapping
void *mmap(void *start, int len,
        int prot, int flags, int fd, int offset)
len bytes
start
(or address
chosen by kernel)
len bytes
offset
(bytes)
0
0
Disk file specified by
file descriptor fd
Process virtual memory

---
Example: Using mmap to Copy Files
Copying a file to stdout without transferring data to user space .
#include "csapp.h"
void mmapcopy(int fd, int size)
{
    /* Ptr to memory mapped area */
    char *bufp;
    bufp = Mmap(NULL, size,
        PROT_READ,
        MAP_PRIVATE,
        fd, 0);
    Write(1, bufp, size);
    return;
}
/* mmapcopy driver */
int main(int argc, char **argv)
{
    struct stat stat;
    int fd;
    /* Check for required cmd line arg */
    if (argc != 2) {
        printf("usage: %s <filename>\n",
        argv[0]);
        exit(0);
    }
    /* Copy input file to stdout */
    fd = Open(argv[1], O_RDONLY, 0);
    Fstat(fd, &stat);
    mmapcopy(fd, stat.st_size);
    exit(0);
}
mmapcopy.c
mmapcopy.c

---
Today
Simple memory system example
Case study: Linux memory system
Memory mapping
Dynamic allocation
Bonus: Implicit free lists

---
Dynamic Memory Allocation
Programmers use dynamic memory allocators (such as malloc) to acquire VM at run time.
For data structures whose size is only known at runtime.
Dynamic memory allocators manage an area of process virtual memory known as the heap.
Application
Dynamic Memory Allocator
Heap
User stack
Top of heap
 (brk ptr)
Heap (via malloc)
Uninitialized data (.bss)
Initialized data (.data)
Program text (.text)
0

---
Dynamic Memory Allocation
Allocator maintains heap as collection of variable sized blocks, which are either allocated or free
Types of allocators
Explicit allocator: application allocates and frees space
E.g., malloc and free in C
Implicit allocator: application allocates, but does not free space
E.g. garbage collection in Java, ML, and Lisp
Will discuss simple explicit memory allocation today

---
The malloc Package
#include <stdlib.h>
void *malloc(size_t size)
Successful:
Returns a pointer to a memory block of at least size bytes
aligned to an 8-byte (x86) or 16-byte (x86-64) boundary
If size == 0, returns NULL
Unsuccessful: returns NULL (0) and sets errno
void free(void *p)
Returns the block pointed at by p to pool of available memory
p must come from a previous call to malloc or realloc
Other functions
calloc: Version of malloc that initializes allocated block to zero.
realloc: Changes the size of a previously allocated block.
sbrk: Used internally by allocators to grow or shrink the heap

---
malloc Example
#include <stdio.h>
#include <stdlib.h>
void foo(int n) {
    int i, *p;
    /* Allocate a block of n ints */
    p = (int *) malloc(n * sizeof(int));
    if (p == NULL) {
        perror("malloc");
        exit(0);
    }
    /* Initialize allocated block */
    for (i=0; i<n; i++)
p[i] = i;
    /* Return allocated block to the heap */
    free(p);
}

---
Assumptions Made in This Lecture
Memory is word addressed.
Words are int-sized.
Allocated block
(4 words)
Free block
(3 words)
Free word
Allocated word

---
Allocation Example
p1 = malloc(4)
p2 = malloc(5)
p3 = malloc(6)
free(p2)
p4 = malloc(2)

---
Constraints
Applications
Can issue arbitrary sequence of malloc and free requests
free request must be to a malloc’d block (or NULL)
Allocators
Can’t control number or size of allocated blocks
Must respond immediately to malloc requests
i.e., can’t reorder or buffer requests
Must allocate blocks from free memory
i.e., can only place allocated blocks in free memory
Must align blocks so they satisfy all alignment requirements
8-byte (x86) or 16-byte (x86-64) alignment on Linux boxes
Can manipulate and modify only free memory
Can’t move the allocated blocks once they are malloc’d
i.e., compaction is not allowed (why?)

---
Performance Goal: Throughput
Given some sequence of malloc and free requests:
R0, R1, ..., Rk, ... , Rn-1
Goals: maximize throughput and peak memory utilization
These goals are often conflicting
Throughput:
Number of completed requests per unit time
Example:
5,000 malloc calls and 5,000 free calls in 10 seconds
Throughput is 1,000 operations/second

---
Performance Goal: Peak Memory Utilization
Given some sequence of malloc and free requests:
R0, R1, ..., Rk, ... , Rn-1
Def: Aggregate payload Pk
malloc(p) results in a block with a payload of p bytes
After request Rk has completed, the aggregate payload Pk is the sum of currently allocated payloads
Def: Current heap size Hk
Assume Hk is monotonically nondecreasing
i.e., heap only grows when allocator uses sbrk
Def: Peak memory utilization after k+1 requests
Uk = ( maxi<=k Pi ) / Hk

---
Fragmentation
Poor memory utilization caused by fragmentation
internal fragmentation
external fragmentation

---
Internal Fragmentation
For a given block, internal fragmentation occurs if payload is smaller than block size
Caused by
Overhead of maintaining heap data structures
Padding for alignment purposes
Explicit policy decisions
(e.g., to return a big block to satisfy a small request)
Depends only on the pattern of previous requests
Thus, easy to measure
Block
Payload
Internal
fragmentation
Internal
fragmentation

---
External Fragmentation
Occurs when there is enough aggregate heap memory, but no single free block is large enough
Depends on the pattern of future requests
Thus, difficult to measure
p1 = malloc(4)
p2 = malloc(5)
p3 = malloc(6)
free(p2)
Oops! (what would happen now?)
p4 = malloc(6)

---
Implementation Issues
How do we know how much memory to free given just a pointer?
How do we keep track of the free blocks?
What do we do with the extra space when allocating a structure that is smaller than the free block it is placed in?
How do we pick a block to use for allocation -- many might fit?
How do we reinsert freed block?

---
Knowing How Much to Free
Standard method
Keep the length of a block in the word preceding the block.
This word is often called the header field or header
Requires an extra word for every allocated block
p0
p0 = malloc(4)
5
block size
payload
free(p0)

---
Keeping Track of Free Blocks
Method 1: Implicit list using length—links all blocks
Method 2: Explicit list among the free blocks using pointers
Method 3: Segregated free list
Different free lists for different size classes
Method 4: Blocks sorted by size
Can use a balanced tree (e.g. Red-Black tree) with pointers within each free block, and the length used as a key
5
4
6
2
5
4
6
2

---
Today
Simple memory system example
Case study: Linux memory system
Memory mapping
Dynamic allocation
Bonus: Implicit free lists

---
Method 1: Implicit List
For each block we need both size and allocation status
Could store this information in two words: wasteful!
Standard trick
If blocks are aligned, some low-order address bits are always 0
Instead of storing an always-0 bit, use it as a allocated/free flag
When reading size word, must mask out this bit
1 word
Size
a
a = 1: Allocated block
a = 0: Free block
Size: block size
Payload: application data
(allocated blocks only)
Payload
Format of
allocated and
free blocks
Optional
padding

---
Detailed Implicit Free List Example
Unused
Start
of
heap
8/0
16/1
32/0
16/1
0/1
Allocated blocks: shaded
Free blocks: unshaded
Headers: labeled with size in bytes/allocated bit
Double-word
aligned

---
Implicit List: Finding a Free Block
First fit:
Search list from beginning, choose first free block that fits:
Can take linear time in total number of blocks (allocated and free)
In practice it can cause “splinters” at beginning of list
Next fit:
Like first fit, but search list starting where previous search finished
Should often be faster than first fit: avoids re-scanning unhelpful blocks
Some research suggests that fragmentation is worse
Best fit:
Search the list, choose the best free block: fits, with fewest bytes left over
Keeps fragments small—usually improves memory utilization
Will typically run slower than first fit
p = start;
while ((p < end) && \\ not passed end
       ((*p & 1) || \\ already allocated
       (*p <= len))) \\ too small
  p = p + (*p & -2); \\ goto next block (word addressed)

---
Implicit List: Allocating in Free Block
Allocating in a free block: splitting
Since allocated space might be smaller than free space, we might want to split the block
4
4
6
2
p
addblock(p, 4)
2
4
4
4
2
void addblock(ptr p, int len) {
  int newsize = ((len + 1) >> 1) << 1; // round up to even
  int oldsize = *p & -2; // mask out low bit
  *p = newsize | 1; // set new length
  if (newsize < oldsize)
    *(p+newsize) = oldsize - newsize; // set length in remaining
} // part of block

---
Implicit List: Freeing a Block
Simplest implementation:
Need only clear the “allocated” flag
  void free_block(ptr p) { *p = *p & -2 }
But can lead to “false fragmentation”
2
4
4
4
2
p
free(p)
2
4
4
4
2
Oops!
malloc(5)
There is enough free space, but the allocator won’t be able to find it

---
Implicit List: Coalescing
Join (coalesce) with next/previous blocks, if they are free
Coalescing with next block
But how do we coalesce with previous block?
2
4
4
4
2
logically
gone
p
free(p)
2
4
4
6
2
void free_block(ptr p) {
   *p = *p & -2; // clear allocated flag
   next = p + *p; // find next block
   if ((*next & 1) == 0)
     *p = *p + *next; // add to this block if
} // not allocated

---
Implicit List: Bidirectional Coalescing
Boundary tags [Knuth73]
Replicate size/allocated word at “bottom” (end) of free blocks
Allows us to traverse the “list” backwards, but requires extra space
Important and general technique!
4
4
4
4
6
6
4
4
a = 1: Allocated block
a = 0: Free block
Size: Total block size
Payload: Application data
(allocated blocks only)
Header
Size
a
Payload and
padding
Format of
allocated and
free blocks
Boundary tag
(footer)
Size
a

---
Constant Time Coalescing
Case 1
Case 2
Case 3
Case 4
Allocated
Allocated
Free
Free
Block being
freed
Allocated
Free
Allocated
Free

---
Constant Time Coalescing (Case 1)
m1
1
m1
1
m1
1
m1
1
n
1
n
0
n
1
n
0
m2
1
m2
1
m2
1
m2
1

---
Constant Time Coalescing (Case 2)
m1
1
m1
1
m1
1
m1
1
n
1
n+m2
0
n
1
m2
0
m2
0
n+m2
0

---
Constant Time Coalescing (Case 3)
m1
0
n+m1
0
m1
0
n
1
n
1
n+m1
0
m2
1
m2
1
m2
1
m2
1

---
Constant Time Coalescing (Case 4)
m1
0
n+m1+m2
0
m1
0
n
1
n
1
m2
0
m2
0
n+m1+m2
0

---
Disadvantages of Boundary Tags
Internal fragmentation
Can it be optimized?
Which blocks need the footer tag?
What does that mean?

---
Summary of Key Allocator Policies
Placement policy:
First-fit, next-fit, best-fit, etc.
Trades off lower throughput for less fragmentation
Interesting observation: segregated free lists (see book) approximate a best fit placement policy without having to search entire free list
Splitting policy:
When do we go ahead and split free blocks?
How much internal fragmentation are we willing to tolerate?
Coalescing policy:
Immediate coalescing: coalesce each time free is called
Deferred coalescing: try to improve performance of free by deferring coalescing until needed. Examples:
Coalesce as you scan the free list for malloc
Coalesce when the amount of external fragmentation reaches some threshold

---
Implicit Lists: Summary
Implementation: very simple
Allocate cost:
linear time worst case
Free cost:
constant time worst case
even with coalescing
Memory usage:
will depend on placement policy
First-fit, next-fit or best-fit
Not used in practice for malloc/free because of linear-time allocation
used in many special purpose applications
However, the concepts of splitting and boundary tag coalescing are general to all allocators